## Slide 1: In-Kernel fast path performance for containers running Telecom Workloads
Nishanth Shyamkumar, Piotr Raczynski, Dave Cremins, Michal Kubiak, Ashok Sunder Rajan - [ Intel Corporation ]

## Slide 2: Telco VNFs
Virtualization of Telecom Network Function, to move away from fixed function paradigm.
Shift from VMs to containers as unit of deployment. Lightweight and quickly deployable. Gaps:
Fast path performance
Scalability
Minimize system integration overhead
Special purpose hardware
Special purpose hardware
Proprietary OS + Software
Proprietary OS + Software
CGNAT
UPF
Commodity Hardware
Open-Source Software
vCGNAT
vUPF
vFirewall

## Slide 3: Container Networking
ns1
ns2
Root/Default
Network Interface card
NW Stack
Root is default host namespace, ns1 & ns2 are container namespaces.
Each container gets its’ own route/arp table, ephemeral ports and netfilter rules.
Interfaces are unique to a network namespace
Namespaces(isolation) and cgroups(Resource control)
Kernel sandboxes a group of processes through PID, mount and network namespaces
Containers use:
NW
Stack
NW
Stack

## Slide 4: Why containers can create processing overhead ?
v
v
v
ns1
ns2
veth
veth
L2 Bridge
Phy if
Traverses root namespace network stack
Netfilter rules to route packet to bridge
Bridge selects the right interface
Traverses ns1/ns2 network stack
CPU cycles spent in Kernel space and for copy operations
L2 Bridge
v
v
v
ns1
ns2
macvlan
macvlan
Macvlan Group
Phy if
MACVLAN
Traverses root namespace network stack
Macvlan Table lookup
Table selects the right interface
Traverses ns1/ns2 network stack
CPU cycles spent in Kernel space and for copy operations
Root
Root

## Slide 5: SRIOV VFs
VF0
VF1
VF2
QP
QP
QP
SRIOV is a HW Virtualization solution
VFs are light-weight PCIe functions
VFs are assigned a pool of Queue pairs
VFs provide scalability
Queue select filtering routes packet to specific queue pair(RSS, Flow Director etc.)
VF interface
ns2
VF interface
ns1
VF interface
ns3
Host

## Slide 6: AF_XDP
Driver
Traffic class
IP + Netfilter
TCP/UDP
AF_INET socket fd
sk_buff
Driver
eBPF program
AF_XDP socket fd
xdp_frame
frame
frame
frame
UMEM
eBPF is a small program that runs at specific hook points in the kernel
AF_XDP socket binds to a specific Queue pair
No sk_buff creation
UMEM is allocated memory in user-space
Lockless rings to transfer frame control
Traditional NW path:
AF_XDP NW path:
User
Kernel

## Slide 7: Zero copy in AF_XDP
frame
frame
frame
Fill ring
Completion ring
Rx ring
Tx
ring
UMEM
SRIOV VF
3. DMA
4. IRQ
5. eBPF
AF_XDP socket fd
6. Update Rx Q
7. Read Rx Q
8. Read frame data from UMEM(ZC)
1. Update Fill ring with empty frame address
2. Program HW RX desc
DRIVER
User
Kernel
HW
QP

## Slide 8: Telecom 4G Architecture
UEs(Mobile phones, Wireless devices) connect to a cell tower/Base station through radio signals
Wired infrastructure carries signals from Base Station to Mobile Core(GTP-C and GTP-U UDP packets)
HSS, MME, PCRF deal with management and User subscription information
SGW – PGW(aka UPF) provides data path to the Internet
Distributed Packet core at MEC site(https://opennetworking.org/news-and-events/press-releases/t-mobile-poland-achieves-production-roll-out-of-omec-onfs-open-source-mobile-evolved-packet-core/)
Image: https://5g.systemsapproach.org/arch.html#main-components
1 MEC Site | 250K devices
Avg packet size | 500 Bytes
Aggregate load@250K devices | 10 Gbps
Aggregate load@250K devices | 2.5 MPPS
Workload for MEC:

## Slide 9: Experimental Test Setup
TGEN used is a software based Pktgen running on DPDK.
TGEN simulates UE, enodeB and provides GTP support
Docker is used to enable the UPF container.
Container Networks for L2 Bridge, MACVLAN, IPVLAN created using Docker commands.
Pipework used to move VF interfaces into Container namespace.
Intel(R) Xeon(R) Platinum 8260 CPU @ 2.40GHz(Skylake) |  |  |  | 
Kernel: Linux 5.15.0-23-generic |  |  |  | 
Test Duration |  | 50 |  | 
PKT_SZ(bytes) |  | 512 |  | 
num_enb |  | 20 |  | 
Flows |  | 8,000 |  | 
pps |  | 2,400,000 |  | 
NW Virtualization modes: L2, MACVLAN, IPVLAN, SRIOV

## Slide 10: Performance Results / Takeaways
Results depicted as ‘Bridging method + NW processing datapath’
L2 bridge least performant due to Netfilter rule matching including NAT translations.
SRIOV + Linux limited due to packet copy(kernel/userspace) and Linux Network stack processing.
SRIOV + afxdp_zc doesn’t need 10 cores to achieve 2MPPS throughput.

## Slide 11: Conclusion:
SRIOV + afxdp_zc provides ~10x performance as compared to other In-kernel mechanisms, lowering TCO.
Kernel space handles Network hardware queue programming and operation, improving system security.
ARP resolution, ifconfig/ip & ethtool statistics availability.
HW IO Virtualization removes bridging overhead, and provides scalability .
Future work:
Integrate into Kubernetes Orchestration framework.
Test scalability and learn about performance thresholds.
Reduce Permissions/privileges to deploy in a pod.
Upstreaming iavf driver modifications.

## Slide 12: References:
Intel 82599 10 GbE Controller Datasheet
AF PACKET V4 and PACKET ZEROCOPY - Magnus Karlsson, Bjorn Topel, and John Fastabend
The Path to DPDK Speeds for AF XDP - Magnus Karlsson and Bjorn Topel
Understanding Linux Network Internals – Christian Benvenuti
Linux Containers and Virtualization – Shashank Mohan Jain
ebpf documentation. ebpf.io/what-is-ebpf
5G Mobile Networks: A Systems Approach, Larry Peterson and Oguz Sunay, https://github.com/SystemsApproach/5G, CC BY-NC-ND 4.0
Petazzoni, J. Pipework software-defined networking for linux containers. https://github.com/jpetazzo/pipework
3GPP. Ts 29.274 technical specification

## Slide 13: References contd.
Høiland-Jørgensen, T.; Brouer, J. D.; Borkmann, D.; Fastabend, J.; Herbert, T.; Ahern, D.; and Miller, D. 2018. The express data path: Fast programmable packet processing in the operating system kernel. CoNEXT ’18 54–66
Kumar, D.; Chakrabarti, S.; Rajan, A. S.; and Huang, J. 2020. Scaling telecom core network functions in public cloud infrastructure. CloudCom
Rajan, A. S.; Gobriel, S.; Maciocco, C.; Ramia, K. B.; Kapur, S.; Singh, A.; Erman, J.; Gopalakrishnan, V.; and Jana, R. 2015. Understanding the bottlenecks in virtualizing cellular core network functions. The 21st IEEE International Workshop on Local and Metropolitan Area Networks

## Slide 14: Notices & Disclaimers:
Performance varies by use, configuration and other factors. Your costs and results may vary. Intel technologies may require enabled hardware, software or service activation.
© Intel Corporation. Intel, the Intel logo, and other Intel marks are trademarks of Intel Corporation or its subsidiaries. Other names and brands may be claimed as the property of others.